## Slide 1
Data Center Management

## Slide 2
Infrastructure in a data center
Modular Cabling Design
A set of racks contains servers, terminal servers, and so forth that need Cat5/6/7 or fiber cable connections.
There are two ways to do this:
■ Cable hosts directly to the switch ports.
■ Use patch panels.
If you use patch panels, all hosts and other devices that need network connections are cabled to ports in a patch panel located close by in the data center.
Patch Panel
Patch panels offer several advantages. They keep connections and cables localized within each physical area. However, you must determine the number of Cat5 and fiber ports needed in each section of the data center and install appropriately sized patch panels. Since patch panels are very difficult to replace,
you must also have extra, unused ports for future use.

## Slide 3
Infrastructure in a data center
Points of Distribution (PODs)
A point of distribution (POD) is a rack with devices, network switches, terminal servers, and patch panels that together provide the infrastructure required
for a number of racks filled with servers and storage.
PODs allow you to group cables and networking equipment required for a set of racks into a single manageable location.
A POD rack contains the following three items:
■Cross-patch ports — Cat5 and fiber connections can be cross-patched. The POD has several ports that are wired to ports in the network room. Each port in a POD must be labeled with the same identifier as its corresponding port in the network room. The wires connecting the POD ports to the ports in the network room must be bundled and run in separate cable trays.

## Slide 4
Infrastructure in a data center
■ Network terminal servers
A terminal server is a device on the network that allows you to log in to a server’s console port, which is usually a serial port.
The terminal server is sometimes known as a portmaster and contains up to 100 or so ports. It can be accessed over the LAN.
Each port within the terminal server is cabled via patch panels to console ports in racked servers.

## Slide 5
Infrastructure in a data center
■ Network subswitches
Small switches used to connect servers to a certain network, such as the administrative or backup network, can be
located inside a POD.
These switches must be connected to the master switch via a link with higher bandwidth than the subswitch-to-host links.
ISP Network Infrastructure
There are several reliable vendors for network equipment, and Cisco is the undisputed market leader.
If the ISP uses equipment from several vendors, it must verify interoperability.
A router may have very high reliability, but its performance may suffer when connected to a switch from another vendor.

## Slide 6
Infrastructure in a data center
The ISP must have a test lab to verify inter-vendor compatibility
before deploying a production architecture, to recreate field problems, and to plan maintenance and upgrade windows with no service disruption.
Other important features of an ISP infrastructure are reliability and tolerance to hardware failures.
Providers should have redundant switches and routers at every network layer.
The network should withstand at least one failure in each layer and continue to function at full performance.
The backup systems should not consist of inferior-capacity hardware.
If it is so, a failure at peak times will cause perceptible performance degradation.

## Slide 7
Infrastructure in a data center
ISP WAN Links
The second part of the network is the ISP’s wide area network (WAN) connection.
The WAN link is composed of two aspects: “transport” and “transit.”
Network “transport” is the path that carries the data and has a certain maximum bandwidth, while the “transit” is the actual data.
But these fast, high bandwidth circuits are a waste without adequate transit.
The ISP must also have reliable and redundant circuits.
Having all the transit on a single pipe is not reliable.
A circuit can have many problems such as a misconfiguration at the central office (CO) or a physically cut fiber in the street.

## Slide 8
Infrastructure in a data center
Therefore, an ISP must have several fiber providers and several transit providers.
There must be a minimum of three of each, and any two should
be able to handle the maximum network traffic.
An ISP with three T1s (at 1.5 Mbits/second) and one T3 (at 45 Mbits/second) does not have redundant circuits, because if the T3 fails, the provider loses more than 90 percent of its capacity.
Several best practices must be followed to ease configuration and maintenance:
■Label your equipment — Label both cable ends and all devices such as switches, routers, and electric breakers. It takes the least effort and time when done during installation. Thereafter, it is a cumbersome task to trace a cable inside a wireway or under the tiles. If a device is having network problems, it is easy to substitute a cable if both cable ends have similar labels.

## Slide 9
Infrastructure in a data center
■ Color code cables — At one company, the data-center crew had a policy of using yellow Cat5 cables for connecting servers to the back-end network and white Cat5 cables for the front-end network.
If you have a backup network, production network, DMZ network, and administration network, you can have cables of four colors.
■ Avoid a tangle of cables — always neatly arrange bundle of
cables connecting data-center devices to the patch panel. It takes deliberate effort to reduce the cable tangles and mess. Always use correct length of Cat5/6/7 or fiber cables to avoid coiling the extra length. Use cable ties to group similar cables. Route cable in cable trays under the tiles to minimize obstruction of air flow. Do not leave loose cables on the floor. All data line terminations must be punched using proper termination tools. Electric punch equipment ensures proper termination and maximum bandwidth over copper cables.

## Slide 10
Infrastructure in a data center
■ Patch panel ports and connections must be verified by the installer — Use Cat5/6/7 and fiber cable testers. They can test up to 1,000-foot-long cables for cable continuity, bad wiring, and open, short, straight-through, or cross pinning. Note that a cable tester should never be used on a live connection.
■ Cable bending radius — Cables must be placed with sufficient bending radius so as not to shear, kink, or damage jackets, binders, or cables, including where cables are coiled for future use or slack.

## Slide 11
Infrastructure in a data center
Network Operations Center (NOC)
The network operations center (NOC) is a dedicated facility staffed with people who monitor the availability of all devices and services
within the data center and respond to any data-center problems.
The NOC has servers, consoles, and network monitoring software such as HP OpenView,IBM Tivoli, Nagios, Prometheus etc.
The software is used to monitor the health, status, and load of each piece of equipment and communication between all devices.
A NOC serves as a central logging point for all alarms and a location for evaluating the present status of the data center.

## Slide 12
Infrastructure in a data center
Simple network monitoring protocol (SNMP) agents can be used with storage devices such as UPS systems, HVAC, and storage devices such as NAS filers and storage area network (SAN) switches to get reports on their status and health on the monitoring software.
Network Monitoring
A critical requirement for data centers is the ability to proactively monitor the availability of all server and network resources.
At a high level, network monitoring is knowing what is happening within your environment.
Network monitoring software is also proactive.
It can be tuned to warn you of impending problems that you must be made aware of such as a sudden burst of network traffic, file systems filling up to a certain threshold, and symptoms of Internet
attacks on your edge routers.

## Slide 13
Infrastructure in a data center
Network monitoring gathers real-time data and classifies it into performance issues and outages.
Performance issues are used to predict the need for future scaling of the environment.
SNMP
Simple network monitoring protocol (SNMP) is the most helpful tool in resource monitoring. It lets you discover what resources are out there and their status. It is used to send information about the health of resources to a central collection host.
SNMP is a protocol that runs over user datagram protocol (UDP).
The daemon is typically called snmpd or snmpdx and runs over port 161. SNMP consists of a number of object identifiers (OIDs) and a management information base (MIB).

## Slide 14
Infrastructure in a data center
A MIB is a collection of hierarchically organized OIDs.
An “object” can be a network interface card, system board temperature, httpd daemon, or router.
By extending the SNMP daemon, any server event or hardware can be monitored.
The SNMP language is composed of three main actions: GET, SET, and TRAP.
GET fetches an OID value from the resource (for example, disk full percentage).
SET configures a value (for example, number of processes allowed for an application).
TRAP watches for an event, and if it occurs, performs some action (for example, restart application).

## Slide 15
Infrastructure in a data center
The SNMP daemon is insecure by default.
It allows for reconfiguration of devices and, if a server or network device is incorrectly configured, data can be exposed.
Therefore, many data centers have SNMP SET operations disabled.
Security is also compromised because of a “community string” and a “private string,” which equate to passwords.
The public string is used for polling and the private string for setting configurations.
Many vendors use the value “public” for public string.
SNMP version 3 supports advanced security such as encrypted sessions and stronger authorization such as Message Digest 5 algorithm (MD5) or data encryption standard (DES) hashes.

## Slide 16
Infrastructure in a data center
In-band monitoring is the capability to change system status through the existing network infrastructure.
Out-of-band monitoring is the capability to control systems not through existing network infrastructure but via a different data network or via a dial-in capability for individual devices.
Several other data center–wide features must be monitored, such as
■ Power from the utility provider
■ UPS status and usage
■ Generator status and usage
■ Leak detection from HVAC and air ducts and from liquid in the HVAC units
■ Temperature in the data center
■ Relative and absolute humidity in the data center
■ Intrusion in the facility

## Slide 17
Infrastructure in a data center
Data-Center Physical Security
A critical component of server and data security is the security of the data center itself.
All entry points and doors to the data center must be controlled by card readers or persons who are physically present to monitor and restrict access of those entering the data center.
Recently biometric readers have been installed at various data centers.
After swiping his or her badge, the employee must place a palm on a biometric reader, which matches the palm prints against an earlier recorded image.
Cameras must be installed not only at the data-center doors but also at the corporate entrances.
Badge access to the data center must not be given to all employees. Only those who must access the data center must be allowed to enter.

## Slide 18
Infrastructure in a data center
Various datacenters have a policy for one-time accesses, where security personnel verify and record if anyone needs to enter.
Functionally there are two types of data centers: co-location (CoLo) data centers and managed-hosting data centers. There are significant differences in security needs between them.
■ Co-location data centers — Hundreds or thousands of customers pass or visit a co-location data center each day. It is therefore vital to control and monitor the visits and list of people who have access to the data center. Despite all precautions and security, visitors can damage other customers’ equipment.
■ Managed hosting data centers — In a secure managed-hosting data center, only a few employees have access to the data center. Customers do not have badges or passes to go inside. If they must go inside, they must be escorted and given temporary badges.

## Slide 19
Infrastructure in a data center
Despite the best physical security, servers can be attacked over the network and that can be far more expedient than gaining physical access.
Therefore, it is critical to have an up-to-date OS image and patch set.
OS and security patches and bug fixes are released daily. Managed hosting providers should have experts who evaluate these patches.
It is often not practical to update the OS proactively on production servers because enterprises want to test the OS on development and stage servers first, and because updates may cause unforeseen application problems.

## Slide 20
Infrastructure in a data center
Data-Center Logical Security
All valuable information of almost all organizations is stored online. It is, therefore, mandatory that the data and servers be protected from people with malicious intent.
Preventing illicit access to the data is of utmost importance.
It is important to keep out people who have no business being physically there (physical security) and to prevent unauthorized access via the network (logical security).
Logical security is making it more difficult for intruders to reach a login prompt on the hosts or other devices.
The telnet port should be closed.
Use ssh instead to log in to UNIX servers.
Protocols using low-number ports (less than 1,024) should be allowed only if necessary.

## Slide 21
Infrastructure in a data center
You must construct more than one layer of authentication before presenting the login prompt and must also allow only a few and necessary users the capability to go beyond these layers.
These users must be forced to authenticate themselves to a central login server, which should be the only machine
having direct access to the consoles.
Data-Center Cleaning
There are many stories on how the cleaning crew knocked power off the storage array because the aisle was narrow or the crew was unaware of the environment.
A data-center setting is different from an office area and, therefore,
does not require regular cleaning or vacuuming.

## Slide 22
Infrastructure in a data center
You must get a cleaning crew in the data center once every 3 or 6 months or as needed, such as after structural (floor, tile, wall, and so forth) changes.
Safety cones must be placed around open tiles and areas that are being damp-mopped.
A prespecified list of equipment and supplies must be used by the cleaning crew.
It is important not to leave particles and debris that could enter the air circulation.
Electrical cords used by the crew must be in good condition and have three pin ground configuration.
The cleaning chemicals must be pH neutral and static dissipative.
Only lint-free and antistatic wipes must be used.
When cleaning the raised floor, care must be taken to avoid disturbing cables routed through the openings in the floor tiles.

## Slide 23
Infrastructure in a data center
Use an approved solution to treat black marks, stains, and smudges on the floor, and scrub them with a medium-grade scrub pad.
Use a Triple-filtration high-efficiency particulate air (HEPA) vacuum cleaner to remove dirt and particles from the top of all accessible floor areas.
Trying to clean below equipment or racks can disrupt operations..
For data centers with raised tiled floors, the space below the tiles must be cleaned.
For data centers without a raised floor, most power and data cables run above the lowered ceiling.
When removing tiles to access the subfloor areas or removing ceiling tiles to access the above-ceiling space, no more than 10 percent of the tiles should be detached at any one time.
Chemicals should not be sprayed directly on any equipment surface.

## Slide 24
Infrastructure in a data center
Quarterly preventive maintenance must include power systems
checks, HVAC and generator servicing, and so forth. All service visits must be coordinated and tracked.
Service plan must include the following:
■ UPS systems and batteries
■ Generator and automatic transfer switch (ATS) equipment
■ Power cables, outlets, subpanels, and circuit breakers
■ Static-switching equipment
■ Free-standing and rack-based power distribution equipment
■ Fire suppression and detection equipment
■ Overhead sprinkler systems
■ Air-conditioning and HVAC units, air ducts, and filters
■ Inlet-air blockages near perforated tiles.

## Slide 25
Infrastructure in a data center
Reasons for Data Center Consolidation
Consolidation is defined as the process of bringing together disconnected parts to make a single and complete whole.
In the data center, this means replacing several small devices with a few, highly capable pieces of equipment to provide simplicity.
The key reason for consolidation is the sprawl of equipment and processes to manage them.
It is absolutely crucial to understand the function of each piece of
equipment and related processes before consolidating them.

## Slide 26
Infrastructure in a data center
It is also critical to understand the key reasons for consolidation:
■ Reduce the number of servers — With distributed computing, each server hosted one application and users logged on to the application from their desktops. One application per server made it easy for each group or department to buy, own, and manage whatever it needed. The servers were cheap and small, and it was easy to buy one every time an application was needed. Actually, each application required more than one server. They needed a development server, staging server (to verify application compatibility before moving code to production servers), training servers (for classes and self-learning), and disaster recovery (DR) servers at a remote site. Up to seven or eight servers, therefore,
were necessary for each application.

## Slide 27
Infrastructure in a data center
■ Increase usage of storage — Each server has its own set of direct-attached storage creating storage islands. If a server runs out of disk space, more must be added to that server, even if other servers in the data center have lots of free storage.
■ Reduce IT processes — There are sets of processes that must be written and followed by everyone for each server and application. Less equipment means fewer processes.
■ Reduce support staff — All the individual equipment needs support staff to ensure it is humming properly. The servers and applications must be tuned, backed up, patched, upgraded, and protected from internal and external threats. Skilled system administrators, database administrators, and network engineers
are hard to find and expensive to retain. Equipment consolidation in a data center will let you get by with fewer support staff..

## Slide 28
Infrastructure in a data center
■ Reduce IT expenses — Replacing several pieces of equipment with fewer and more capable hardware components helps reduce expenses in several ways. It makes the environment simpler and easier to manage, reduces hardware maintenance expenses, takes up less of the costly data center floor space, and needs fewer processes and staff.
■ Increased service reliability — With equipment and process consolidation, it becomes easier to centralize management of the IT environment. With fewer processes, the environment can be managed more effectively, which, in turn, gives higher service reliability and uptime and reduced fines caused by missed service level agreement (SLA) commitments.
This is one of the most important reasons why several organizations have started consolidating their hardware and processes.

## Slide 29
Infrastructure in a data center
Consolidation Opportunities
The initial and obvious target for consolidation is the number of servers and storage devices. However, as the consolidation process starts off, several other equipment and processes seem ideal candidates. At a high level, you should think of consolidation as a way to reduce the number of devices and number of ways to manage the devices.
Server Consolidation
Some organizations have hundreds and others have thousands of servers. Whatever the number, it is too many for the in-house team to manage. Consolidation is necessary and there are two ways to do so: vertical scaling and horizontal scaling. Vertical scaling specifies how you can reduce the server count by running multiple applications on fewer but well-beefed-up servers. Horizontal scaling allows you to bear increased workload by distributing it across
several replicated servers.

## Slide 30
Infrastructure in a data center
Once you are aware of these consolidation techniques, you can further refine the consolidation by grouping the servers into three broad categories.
■ Front-end servers — These servers are closest to the user community. The most common technique here is horizontal scaling, where incoming load is distributed among the servers by a load-balancing switch. The architecture calls for many low-end, easy-to-replace servers that have access to the same data on shared or dedicated storage. It is not possible to reduce the numbers of servers, but simpler management practices can be standardized for the set of servers to result in lower total cost of
ownership.

## Slide 31
Infrastructure in a data center
■ Application servers — These run applications and middleware. In most cases, it is possible to replace a large number of application servers with fewer large servers (vertical consolidation).
■ Back-end database servers — These are high-end servers that run mission critical databases or applications. They have a large amount of compute resources and are clustered to ensure almost 100 percent uptime. These are ideal candidates for vertical consolidation.

## Slide 32
Infrastructure in a data center
Storage Consolidation.
It is estimated that the amount of storage doubles every two years. The ever increasing volume of data and its management has made the cost of storage a significant portion of the total cost of ownership of an IT environment. All this has led to various ways to consolidate storage.
Following are important advantages of storage consolidation:
■ Increased storage utilization — A recent study showed that an average about of 20 percent to 40 percent of storage space is utilized if it is accessible by only one server. If a server requires more storage, it is a lot easier to buy new storage and add it, rather than migrate storage connected to another server (although other servers may contain a lot of unused, free space). The utilized percentage is higher if storage is accessible by several servers.

## Slide 33
Infrastructure in a data center
■ Easier data backup and recovery — Backing up disparate storage devices requires more configuration and time than the same quantity of storage within a subsystem.
■ Affordability — It is easier and more affordable to increase the reliability, availability, and serviceability (RAS) and remote data replication for a single high-end storage subsystem than for several small disconnected storage devices.
Following are four types of storage consolidations:
■ Storage consolidation by consolidating servers
■ Various servers linked to a single storage subsystem
■ Consolidation with storage area network (SAN)
■ Consolidation with network attached storage (NAS)

## Slide 34
Infrastructure in a data center
Storage Consolidation by Consolidating Servers
As applications (previously running on separate hosts) are moved to a single host, the storage must also be moved.
The consolidated storage is now available to all the applications.
It is a single Server with a very high storage capacity.
Various Servers Linked to a Single Storage Subsystem
This form of storage consolidation is the most popular type. Applications from various servers can be migrated to a single server if the servers are of the same platform (UNIX, Windows, and so forth). IT organizations rarely run enterprisewide applications on one vendor’s platform, but rather have a mix of Windows,Linux, and other operating systems. Instead of providing storage islands for each platform, a single, large storage subsystem can be used for all platforms. It is important to ensure that storage drivers are available for various platforms.

## Slide 35
Infrastructure in a data center
Consolidation with Storage Area Network (SAN)
SAN is a set of storage-switching devices that connect a set of servers to a shared storage pool. SAN could be one or more switches or hubs. Any server connected to the SAN fabric can access and use any of the storage devices connected to it.
Consolidation with Network Attached Storage (NAS)
Unlike the previous three consolidation forms, NAS allows servers to access storage over the network using networking protocols such as Network File System (NFS), Server Message Block (SMB), Common Internet File System (CIFS), Hypertext Transfer Protocol (HTTP), and File Transfer Protocol (FTP).

## Slide 36
Infrastructure in a data center
Network Consolidation
Consolidating a heterogeneous network into a robust, homogeneous environment requires good process and people management.
When faced with several heterogeneous networks, any one of the following three approaches can be taken to combine the network topologies and processes:
■ The first strategy is to maintain a diverse network and consolidate people. There are no equipment or network topology changes. However, the headcount is reduced and a combined team is tasked to manage all the existing networks. All the networks compete for the reduced personnel time and the result is inferior network management and support.

## Slide 37
Infrastructure in a data center
■ The second strategy is to select a pre-existing network and expand it to provide services to the entire organization. Servers and devices from other networks are slowly migrated to the selected network. It is important to select the network on technical merit and not on prior ownership or political pressures. Because of the high business dependence on network services, a poor selection or consolidation plan will result in chaos, upheaval, reduced availability, and unplanned outages.
■ The third strategy is hybridization. It involves a review and unit-cost analysis of all existing networks and new candidate solutions. The goal is to architect a solution that is a either a hybrid of the existing networks or a completely new network. The next step (after review) is to create a detailed, stage-by-stage migration from the existing network to a new solution. The plan must pay attention to application dependencies and acceptable latencies for users.

## Slide 38
Infrastructure in a data center
The impact of server and storage consolidation on network devices can be adverse or favorable. The consolidation of servers and applications to fewer physical locations will require a higher network bandwidth in those locations if traffic is mostly from users and applications outside the consolidated applications.
Application Consolidation
The first task is to select applications that are right for consolidation and those that are not. It is easy to identify and earmark applications that will not be consolidated. These include the following:
■ Geographically dispersed servers configured for disaster recovery purposes
■ Security servers such as gateways, terminal servers, firewalls, and virtual private network (VPN) servers

## Slide 39
Infrastructure in a data center
■ Servers whose access is highly restricted because they contain sensitive data or logs
■ Software whose vendors have definite needs of a dedicated server for proper functioning
Now identify applications that can be consolidated:
■ Database instance — A common consolidation technique is to place several instances of a particular database on the same server. However, you should not place different databases (such as Oracle, DB2, Sybase, or Informix) on the same server because of their kernel and patch requirements.
■ Application sets — It is important to identify a pattern in the applications usage. Which set of applications send data to or receive data from another group of servers? Because applications process data sequentially and often do not simultaneously compete for the same server resources, the applications can be consolidated to fewer servers. The net result is decreased network traffic and improved communication between applications.

## Slide 40
Infrastructure in a data center
It is important to distinguish between two types of bindings between applications: active and loose.
In active binding, the applications have a two-way and prompt interaction.
Examples are the communication between Web and middleware applications and between ERP applications and database servers.
If these tightly bound applications are moved to one high-end server, the result would be decreased network load and faster interaction.
In loose bindings, the applications receive and process data and then transmit it to another server.
All these happen at predetermined times.
An example would be a database server that transfers its data to the reporting server once every night.
Consolidating actively bound applications to a single server decreases the network load and has better payoff.

## Slide 41
Infrastructure in a data center
Service Consolidation
This is another popular consolidation used in corporations with several departments. Historically, every department implements its own services (such as file, print, and authentication) using software from vendors it is most conversant with. Soon there are too many such services in the organization. The complexity and cost of administration increases dramatically. Users from different
departments cannot share information and services because of software incompatibilities. A common example is authentication services such as Lightweight Directory Access Protocol (LDAP).
The solution is to configure a single enterprise-wide service and deploy it across all departments. Many corporations have consolidated authentication services to a single sign-on application for all Web-based applications that require user login and password. Printers on some campuses have also been consolidated to a single print server that manages all network printer queues.

## Slide 42
Infrastructure in a data center
Process Consolidation
Some environments within a data center are chaotic, with servers rebooting all the time, high CPU, swap and disk usage alerts, low service quality, and reduced data availability.
When such an environment is compared with another environment that runs in a problem-free and smooth manner, it is easy to see that the missing ingredient is a set of well-followed standards and processes.
To improve service quality and availability, and to reduce operational costs, you must consolidate processes and train support staff on those processes.

## Slide 43
Infrastructure in a data center
Staff Consolidation
One important outcome of well-consolidated resources and processes is standardization and ease of management.
This, in turn, leads to reduced requirement of the number of support staff.
Another aspect of staff consolidation is that staff must be well-trained on the data center processes.
It is estimated that 80 percent of service outages are caused by staff negligence or process breakdown, and 20 percent is caused by hardware or technical faults.
It is necessary to address people and standards issues to avoid low service quality and reduced availability.

## Slide 44
Infrastructure in a data center
Consolidation Phases.
Following are the main consodilation phases :
■ Phase 1: Study and document the current environment.
■ Phase 2: Architect the target consolidated environment.
■ Phase 3: Implement the new architecture.
■ Phase 4: Control and administer the consolidated environment.

## Slide 45
Infrastructure in a data center
Phase 1: Study and Document the Current Environment
This is the first and the most important stage.
During this stage, you understand all facets of the IT environment that are targets for consolidations, as well as collect and document all technical information.
What are the servers, storage, networking, and application requirements? How do these intercommunicate and how do they depend on each other?
This phase can be very detailed and time-consuming.
Therefore, it is vital to decide on the amount of details required and then stick to the requirement.
It requires an in-depth technical and business know-how to judge the extent of information required for the entire project.

## Slide 46
Infrastructure in a data center
Evaluate Application Requirements
The purpose of this step is to understand the function of each application, as well as the flow of data from server to server and process to process.
Evaluate Hardware Infrastructure
After applications have been profiled and documented, it is time to assess the hardware platforms. The important task at hand is to verify the current inventory along with the configuration and to estimate the resource utilization. The depth of these investigations must be limited to the server and applications that will be consolidated.

## Slide 47
Infrastructure in a data center
Evaluate Storage Requirements
Over the last few years, the demand for more and more storage has far exceeded the demand for more servers or network bandwidth. Adding storage to existing servers was least disruptive and, consequently, it was added whenever needs arose.
While assessing storage requirements for the subsequent phases of consolidation, you must document the following:
■ Storage hardware
■ Logical configuration
■ Data
Evaluate Networking Requirements
Network assessment is necessary to make provisions for enough bandwidth in the new architecture. The network is used not only for server communication but also for NAS and for storage over IP.

## Slide 48
Infrastructure in a data center
Evaluate Operations Requirements
Staff and the processes they follow are always an important, and yet overlooked, part of an assessment process.
Studies have shown 80 percent of data center and service outages are caused by people or process mishaps, and only 20 percent are caused by purely technical problems.
It is essential to identify the processes and make suitable updates to make them pertinent to the post consolidation environment.
It is also important to update the staff skills regarding various data center activities (such as server, storage, and network management, security, disaster recovery, asset management, and hardware resource utilization management).

## Slide 49
Infrastructure in a data center
Evaluate Risk
Consolidation, like any other IT project, has its fair share of risks. Like all risks, the main risk is looking the other way when it is staring you in the face.
You do not have to like it, but you have to understand all the risks and implement ways to alleviate them.
Phase 2: Architect the Target Consolidated Environment
In this phase, a consolidated design is architected using data from the evaluation phase. The design must specify overall organization of servers, storage devices, and network equipment, as well as
the relationships between them. This stage does not specify specific hardware models, server resources, equipment details, or software versions or patches.

## Slide 50
Infrastructure in a data center
There are several steps in design:
1. Analyze the collected data.
2. List architectural requirements.
3. Create an initial architecture.
4. Size all equipment.
5. Create a prototype of the proposed solution.
6. Test the prototype.
7. Revise the proposed architecture.
8. Document the proposed architecture..

## Slide 51
Infrastructure in a data center
Phase 3: Implement the New Architecture
After evaluating the existing environment, creating a design proposal, and testing a prototype, and with the revised documentation in hand, it is time to start building the consolidated design.
Following are the main steps in the implementation phase:
1. Draft all low-level specifications.
2. Construct the new environment.
3. Create a data migration process.
4. Back up data in the old environment.
5. Migrate data and application services to the new environment.
6. Train the operations staff

## Slide 52
Infrastructure in a data center
Phase 4: Control and Administer the Consolidated Environment
Sticking a new environment within an otherwise smooth operation is annoying. A consolidated set of applications sharing the same servers, resources, and infrastructure is an added nuisance. It requires diligent planning and tough operational processes to allay the impact.
It is crucial to develop a set of robust policies and operational procedures to improve the following:
■ Increase accountability
■ Increase availability
■ Increase security

## Slide 53
Infrastructure in a data center
To maintain an acceptable level of accountability, service availability, and security, it is necessary to identify and prioritize areas that can most negatively jeopardize required service levels.
■ Execution control — This covers policies for scheduling various data center resources among the users of the consolidated environment. The resources include staff time and hardware such as servers, network, and storage.
■ Problem management — This is about identifying and resolving problems, hopefully before they flare up.
■ Change control — This includes things such as scheduling activities or changes in the environment, performing the work, and documenting the results of the change. These changes include hardware changes, reboots, software upgrades, configuration changes, and user account changes.

## Slide 54
Infrastructure in a data center
■ Asset control — In an environment that is not centralized, there is a one application-to-one-server relationship. Each user group knows of the servers that it uses. In a consolidated environment, the asset control team (or person) must set up a computing model to determine the resource usage by each user group. This is necessary for hardware and IT staff charges that must be based on usage.
■ Personnel management — This includes staff recruitment, training, and proper use of the staff-at-hand. Staff consolidation is an important goal for centralizing services. You must ensure that the right number of employees, with the correct skill sets, are assigned to each work.

## Slide 55
Infrastructure in a data center
Server Sizing and Capacity Planning
Server sizing is an estimate of hardware requirements based on applications, anticipated activity, and satisfactory performance levels.
Capacity planning is a two-phase process.
In Phase I, you run tests to measure utilization and performance given a certain amount of hardware resources and activity.
In Phase 2, you project the amount of hardware resources required to support larger workloads.
The distinction from sizing is that you have technical performance data to make a projection, rather than simply providing an
estimated quantity.

## Slide 56
Infrastructure in a data center
Disaster Recovery.
A disaster is defined as an extended outage of mission-critical applications and data because of a lack of network- or computer-processing capabilities.
If the outage does not cause loss of revenue, it may take a couple days of outage to qualify it as a disaster.
The key to disaster recovery (DR) is planning and identifying an optimal recovery procedure that incurs minimum delay.
DR planning involves configuring a remote standby site that can take over mission-critical applications and operations within a reasonable time if disaster strikes the primary site.

## Slide 57
Infrastructure in a data center
Here are some natural causes and man-made causes of disasters:

## Slide 58
Infrastructure in a data center
Following are the five phases of Disaster Recovery
■ Phase 1 — Find the funds.
■ Phase 2 — Assess existing environment and risks.
■ Phase 3 — Create DR procedures.
■ Phase 4 — Test the procedures.
■ Phase 5 — Adjust your DR plan to site changes and technical
Advancements.
A disaster-tolerant site is one whose data is replicated to a remote site either synchronously or asynchronously and in which applications continue to be online, even in the event of a complete failure of the data center or building.